## Slide 1: r01lib and r01device C++ libraries for easy MCU operation
CAS-Japan
2024-December-13
Akifumi OKANO

## Slide 2: Executive summary
Libraries are available which enables to write I3C/I2C/SPI applications easy on MCX mocrocontrollers!
Same application code works on any supported MCX boards
‘r01lib’ and ’r01device’ are the libraries provides simple API to operate MCU features/peripherals
The libraries are suitable for writing demo code and hands-on for introducing devices
Any comment, request, bug-report and pull-request are welcome 
  → akifumi.okano@nxp.com

## Slide 3: Supported MCU boards
FRDM-MCXN947
FRDM-MCXN236
FRDM-MCXA153
FRDM-MCXA156
NEW!

## Slide 4: For instance.. : Evaluation board sample code can run any MCX with r01lib
FRDM-MCXN947
FRDM-MCXA156
SDK
SDK
r01lib (+ r01device)
App
App
App
App
App
RTC
(I²C/SPI)
GPIO
(I²C/SPI)
LCD
(I²C)
Temp sens.
(I3C)
LED
(I²C/SPI)
FRDM-MCXN236
SDK
FRDM-MCX boards
SDK for each MCX boards
Drivers for each MCU and peripherals
“r01lib” is an abstraction layer for MCXs
Abstracting I3C, I²C, SPI, GPIO, Timer, Interrupt with simple C++ API
Application for each ARD boards
Written on “r01lib”. Same code runs on any MCX boards
R01 Arduino shield (ARD) boards
FRDM-MCXA153
SDK

## Slide 5: Hardware/Software structure
FRDM-MCXNxxx / FRDM-MCXAxxx
R01 products
MCUXpresso SDK
r01lib
r01device
Application
Software
Hardware
API cals
Register access
I²C/I3C/SPI/GPIO

## Slide 6: How will it be looked like?
The r01lib is delivered as a part of sample code
The r01lib is made as library project
for each MCU boards
Various sample code projects those will be linked with r01lib library

## Slide 7: API documents are available

## Slide 8: r01lib
00
MCU abstraction layer

## Slide 9: Library for abstracting MCU on MCUXpresso Simple interface to write sample code
r01lib = A driver collection for MCU’s bus/pin operations
Problem so far
  The MCUXpresso SDK drivers are available in low level. It is good to software engineer who needs to derive maximum MCU performance but not easy to use for everyone
  Assigning MCU pin requires low level port and clock settings or use of “Config Tool”
  MCX desn’t have user friendly development environment like other MCUs yet. For instance, “Mbed” and “Arduino” are not adopted for MCX those are popular SDKs providing simple API with abstracting MCUs.
What has been done
  Made a small set of library which controls I3C, I2C, SPI, GPIO, pin-interrupt and timer
  The user-interface is made like Mbed SDK: Features and pins can be operated with high level simple interface
  wait() function to control timing
  The library can be bundled with demo code as a MCUXpresso project
  The library is ported to FRDM-MCXN947, FRDM-MCXN236, FRDM-MCXA156 and FRDM-MCXA153. The library make possible to run same code on both evaluation boards

## Slide 10: Available APIs
DigitalInOut / DigitalIn / DigitalOut class
BusInOut / BusIn / BusOut classes
InterruptIn class
Ticker class
I2C class
I3C class
SPI class
Wait function

## Slide 11: r01lib operation sample
01
Simple API

## Slide 12: Sample 0 : DigitalOut LED blink
#include "r01lib.h"
DigitalOut led( GREEN );
int main(void)
{
while ( 1 )
{
led = !led;
wait( 0.5 );
}
}
GPIO can be controlled by simple interface
No need to care about GPIO registers
Pin names are defined in “component/r01lib/io.h”
Wait() takes float number (seconds). Down to microsecond resolution

## Slide 13: Sample 2 : DigitalOut Flips GPIO pins
#include "r01lib.h"
DigitalOut d5( D5 );
DigitalOut d6( D6 );
DigitalOut d7( D7 );
int main(void)
{
int count = 0;
while ( 1 )
{
d5 = (count >> 0) & 0x01;
d6 = (count >> 1) & 0x01;
d7 = (count >> 2) & 0x01;
count++;
}
}
It can handle multiple GPIOs
Input can be done by DigitalIn and DigitalInOut classes

## Slide 14: Sample 3 : I2C Low level P3T1755 access
#include "r01lib.h"
I2C i2c( I2C_SDA, I2C_SCL );
int main( void )
{
constexpr uint8_t address = 0x4C;
uint8_t w_data[] = { 0 };
uint8_t r_data[ 2 ];
while ( true )
{
i2c.write( address, w_data, sizeof( w_data ), I2C::NO_STOP );
i2c.read( address, r_data, sizeof( r_data ) );
printf( "0x %02X %02X\r\n", r_data[ 0 ], r_data[ 1 ] );
wait( 1 );
}
}
I2C class provides a simple interface to perform transfer

## Slide 15: Available pins
02
FRDM-MCXN947
FRDM-MCXN236
FRDM-MCXA156
FRDM-MCXA153

## Slide 16: Pins
FRDM-MCXN947

## Slide 17: FRDM-MCXN947 Arduino socket
BLUE
IOREF (3.3V)
3.3V Regulated Out
5.0V USB Out
0V
0V
NC
NC
nR
VOUT
VU
GND
GND
REF
A2
A3
A4
A5
D7
D0
D5
D4
D3
D2
D1
D6
0V
D8
D9
I2C
D13
D12
D11
D10
sda
scl
AREF
GND
I3C
sda scl
RED
GREEN
D19
D18
SPI
sclk
miso
mosi
cs
I2C_SDA
I2C_SCL
I3C_SDA
I3C_SCL
= Pin names which can be used in the code
* Note: A5 pin is tied to 10kΩ pull-up and 100nF capacitor to GND on board
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name

## Slide 18: FRDM-MCXN947 mikroBUS socket
0V
GND
= Pin names which can be used in the code
0V
GND
3.3V Regulated Out
5.0V USB Out
VOUT
VU
MB_CS
MB_PWM
MB_INT
MB_RX
MB_TX
MB_SCL
MB_SDA
MB_MOSI
MB_MISO
MB_SCK
MB_RST
I2C
scl
sda
I3C
sda scl
I3C_SDA
I3C_SCL
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name

## Slide 19: Available pins N947

## Slide 20: Pins
FRDM-MCXN236

## Slide 21: FRDM-MCXN236 Arduino socket
BLUE
IOREF (3.3V)
3.3V Regulated Out
5.0V USB Out
0V
0V
NC
NC
nR
VOUT
VU
GND
GND
REF
A2
A3
A4
A5
D7
D0
D5
D4
D3
D2
D1
D6
0V
D8
D9
I3C
D13
D12
D11
D10
sda
scl
AREF
GND
RED
GREEN
D19
D18
SPI
sclk
miso
mosi
cs
I3C_SDA
I3C_SCL
A0
A1
I2C
sda
scl
I2C_SDA
I2C_SCL
BLUE
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
= Pin names which can be used in the code

## Slide 22: FRDM-MCXN236 mikroBUS socket
0V
GND
0V
GND
3.3V Regulated Out
5.0V USB Out
VOUT
VU
MB_CS
MB_PWM
MB_INT
MB_RX
MB_TX
MB_SCL
MB_SDA
MB_MOSI
MB_MISO
MB_SCK
MB_RST
I2C
scl
sda
MB_AN
RED
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
= Pin names which can be used in the code

## Slide 23: Available pins N236

## Slide 24: Pins
FRDM-MCXA156

## Slide 25: FRDM-MCXA156 Arduino socket
IOREF (3.3V)
3.3V Regulated Out
5.0V USB Out
0V
0V
NC
NC
nR
VOUT
VU
GND
GND
REF
D7
D0
D5
D4
D2
D1
D6
0V
D8
D9
I2C/I3C
D19
D18
D13
D12
D11
D10
sda
scl
AREF
GND
I2C_SDA
I2C_SCL
RED
D3
A2
A3
A4
A5
A0
A1
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
GREEN
I3C_SDA
I3C_SCL
= Pin names which can be used in the code
SPI is not available on D10~D13
To use I²C on A4/A5, remove R75 and R76

## Slide 26: FRDM-MCXA156 mikroBUS socket
0V
GND
5.0V USB Out
VU
MB_PWM
MB_INT
MB_RX
MB_TX
MB_SCL
MB_SDA
I2C
scl
sda
0V
GND
3.3V Regulated Out
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
I2C
scl
I2C
sda
VOUT
MB_CS
MB_MOSI
MB_SCK
MB_RST
MB_AN
cs
sclk
miso
mosi
SPI
MB_MISO
= Pin names which can be used in the code

## Slide 27: Available pins A156

## Slide 28: Pins
FRDM-MCXA153

## Slide 29: FRDM-MCXA153 Arduino socket
IOREF (3.3V)
3.3V Regulated Out
5.0V USB Out
0V
0V
NC
NC
nR
VOUT
VU
GND
GND
REF
D7
D0
D5
D4
D2
D1
D6
0V
D8
D9
I2C/I3C
D19
D18
D13
D12
D11
D10
sda
scl
AREF
GND
I3C
scl
sda
I2C
scl
sda
I2C_SDA
I2C_SCL
I3C_SDA
I3C_SCL
BLUE
RED
GREEN
D3
The I3C can be routed to D18 and D19 pins by declaring as I3C( I2C_SDA, I2C_SCL )
A2
A3
A4
A5
A0
A1
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
SPI
sclk
miso
mosi
cs
= Pin names which can be used in the code

## Slide 30: FRDM-MCXA153 mikroBUS socket
0V
GND
5.0V USB Out
VU
MB_PWM
MB_INT
MB_RX
MB_TX
MB_SCL
MB_SDA
I2C
scl
sda
All pin sockets can be used by defining pin like “P1_17”
This page shows pin sockets having special name
0V
GND
3.3V Regulated Out
I2C
scl
I2C
sda
VOUT
MB_CS
MB_MOSI
MB_SCK
MB_RST
MB_AN
MB_MISO
= Pin names which can be used in the code

## Slide 31: Available pins A153

## Slide 32: Example of defining I3C pins from code on FRDM-MCXA153
D7
D0
D5
D4
D2
D1
D6
0V
D8
D9
I2C/I3C
D19
D18
D13
D12
D11
D10
sda
scl
AREF
GND
I3C
scl
sda
I2C
scl
sda
I2C_SDA
I2C_SCL
I3C_SDA
I3C_SCL
BLUE
RED
GREEN
D3
#include "r01lib.h"
I2C i2c( I2C_SDA, I2C_SCL );
#include "r01lib.h"
I3C i3c( I3C_SDA, I3C_SCL );
#include "r01lib.h"
I3C i3c( I2C_SDA, I2C_SCL );
For instance, in I3C case, the signals can be changed to re-route the signals to D18 and D19 by giving arguments for constructor.

## Slide 33: Example of defining I3C pins from code on FRDM-MCXN947
BLUE
D7
D0
D5
D4
D3
D2
D1
D6
0V
D8
D9
I2C
D13
D12
D11
D10
sda
scl
AREF
GND
I3C
sda scl
RED
GREEN
D19
D18
SPI
sclk
miso
mosi
cs
I2C_SDA
I2C_SCL
I3C_SDA
I3C_SCL
#include "r01lib.h"
I2C i2c( I2C_SDA, I2C_SCL );
#include "r01lib.h"
I3C i3c( I3C_SDA, I3C_SCL );
#include "r01lib.h"
I3C i3c( I2C_SDA, I2C_SCL );
On FRDM-MCXN947, the I3C signals cannot be assigned to D18 and D19 because hardware doesn’t allow this configuration

## Slide 34: r01device
03
R01 product operation sample library

## Slide 35: Library for R01 products operation on MCUXpresso Simple interface to write sample code
r01device = A class driver correction for r01 device operations
Delivered as a part of r01lib
Abstracting device operation
  To present devices’ main features with simple interfaces
  User don’t need to care register level operation
  If user need to access register, it can be done through register access APIs

## Slide 36: Available device classes
All available classes can be found on online document

## Slide 37: r01device operation sample
04
Simple API

## Slide 38: Sample 1 : P3T1755 Interface to temp sensor
#include "r01lib.h"
I3C i3c( I3C_SDA, I3C_SCL );
P3T1755 p3t1755( i3c );
int main(void)
{
float temp;
i3c.ccc_broadcast( CCC::BROADCAST_RSTDAA, NULL, 0 );
i3c.ccc_set( CCC::DIRECT_SETDASA, 0x48, 0x08 << 1 );
p3t1755.address_overwrite( 0x08 );
while ( true )
{
temp = p3t1755;
printf( "Temperature: %8.4f˚C\r\n", temp );
wait( 1 );
}
}
P3T1755 class makes an interface for the I3C device
Register level access is abstracted
This sample is using CCC interface in I3C class

## Slide 39: Sample 2 : PCA9955B Interface to LED driver
#include "r01lib.h"
#include "led/PCA9955B.h"
I2C i2c( I2C_SDA, I2C_SCL );
PCA9955B ledd( i2c );
int main(void)
{
ledd.begin( 1.0, PCA9955B::ARDUINO_SHIELD );
while ( true )
{
ledd.pwm( 0, 1.0 );
wait( 0.1 );
ledd.pwm( 0, 0.0 );
wait( 0.1 );
}
}
PCA9955B class makes an interface for the LED driver
PWM can be controlled through instance method

## Slide 40: Sample 3 : PCF2131 Interface to RTC
#include "r01lib.h"
#include <time.h>
#include "rtc/PCF2131_I2C.h”
I2C i2c( I2C_SDA, I2C_SCL );
PCF2131_I2C rtc( i2c );
int main(void)
{
while ( true )
{
time_t current_time = rtc.time( NULL );
printf( "time: %s", ctime(&current_time) );
wait( 1 );
}
}
PCF2131 class makes an interface for the RTC
The interface data format is compatible with “time.h” in C standard lib.

## Slide 41: Repository
05
Access to the code

## Slide 42: Repo
https://github.com/teddokano/r01lib_MCUXpresso
  Including both r01lib and r01device source code
  This repo including sample/test code for available features
    DigitalInOut, DigirtalIn, DigitalOut, BusInOut, BusIn, BusOut, InterruptIn, Ticker, I3C, I2C, SPI classes
The device usage samples with ‘r01device’ are available in https://github.com/teddokano/r01projects
  This repo is hidden by some reasons. But all you are welcome to join to see this. Please let OKANO know your GitHub to invite!
  Sample code to operate ..
    NAFE13388, PCA8561, PCA9957, PCAL6534, PCAL9722, PCF2131(I²C&SPI), P3T1755

## Slide 43: How to start writing your own code Write your code
Choose template project and overwrite
source/main.cpp .
If needed, new files (.c/.cpp/.h) can be added in source/ folder.

## Slide 44: How to start writing your own code Code exporting: step1
Rename the project
Right click on the project and choose “Rename…” from pop-up menu

## Slide 45: Code distribution: step2
Choose the project(s)
Click on “Export project(s) and reference to archive (zip)”

## Slide 46: History
06

## Slide 47: Document revision history
Date | Updates
2024 Mar 21 | Initial version
2024 May 29 | Pin name information added
2024 Jul 17 | FRDM-MCXN236 support added
2024 Dec 09 | FRDM-MCXA156 support added
2024 Dec 10 | Available pins tables updated to clarify the pins which have multiple names
2024 Dec 13 | Picture of “How will it be looked like?” and “API documents are available” pages are replaced